## Slide 1: Quasi-stationary WAVEWATCH III
André van der Westhuysen
The WAVEWATCH III Team + friends
Marine Modeling and Analysis Branch
NOAA / NWS / NCEP / EMC
NCEP.list.WAVEWATCH@NOAA.gov
NCEP.list.waves@NOAA.gov

## Slide 2: Outline
Covered in this lecture:
  Action balance equation and solution methods
  Quasi-stationary operation of WWIII
  Alternative QS approaches
  Field case: Hurricane Gustav

## Slide 3: Action balance equation
  Required physics for nearshore application already present
  Eulerian approach on rectangular, curvilinear or unstructured grids
  Explicit vs. Implicit implementations
  CFL constraints and nearshore application

## Slide 4: Resolving coastal scales
Current WWIII model
grid mosaic
Max. coastal resolution = 4 arc min (7.5 km)
Desired nearshore application
Nearshore resolution: < 100 m

## Slide 5: Performance comparison: Explicit vs. Implicit
Chart: 
| SWAN | WWIII | WT-HigRes | WT-LowRes
Run Time [Min] | 50 | 328 | 155 | 16
%CPU Use | 68 | 80 | 99 | 72
Memory Use [Gb] | 20 | 22 | 180 | 36
WFO MFL Alpha testing site
1 arc-min grid
96 h forecast, dt – 600 s

## Slide 6: Quasi-stationary operation of WWIII
Residence time
Global input/output interval
Quasi-stationary conditions
where:
Time stepping can be accelerated:
  where ,
  with  a constant = 1.2

## Slide 7: Test case: Idealized wave propagation
fp = 0.33 Hz, Std dev. = 0.01 Hz
Dir = 270 oN, monochromatic, long-crested

## Slide 8: Approach 1: Discontinuous time stepping, discontinuous stationary BC

## Slide 9: Approach 2: Discontinuous time stepping, discontinuous nonstationary, phase-shifted BC

## Slide 10: Field case: Hurricane Gustav (Aug-Sept 2008)
Data: Chen et al. (2010)

## Slide 11: Results: H Gustav (Nonstationary WWIII)
Grid 1
Grid 2
Grid 3
Grid 4
Grid 5
Grid 5: tn = 5 s
Run time = 67 min
(512 cores on IBM Power6 Cluster)

## Slide 12: Results: Hurricane Gustav, QS WWIII

## Slide 13: Results: Hurricane Gustav, QS WWIII
Wave-field dependent ts
Constant ts = 1800 s

## Slide 14: Conclusions
  If the residence time ts in nearshore domains is shorter than the input/output interval, quasi-stationary conditions develop, and a saving in computational time of the explicit model is possible.
  Quasi-stationary approach is proposed with (i) discontinuous time stepping, and (ii) nonstationary, discontinuous, phase-shifted BCs.
  With variable ts computed from wave field: Local computational time savings of up to 50% (depending on domain and wave condition), with errors below 1% and no spurious phase lag.
  With constant ts: Greater constant savings in computational time (50% total), but with greater error (Hm0 < 5%; Tm01 < 2%).
  Run time is about 20 times longer than an equivalent nonstationary SWAN run (with t = 10 min, no. iter = 3), but CFL condition is adhered to, and error can be controlled.
  Future: QS implementation for WWIII Multigrid.

## Slide 15: The end
End of lecture