## Slide 1: Parallel implementation
Hendrik Tolman
The WAVEWATCH III Team + friends
Marine Modeling and Analysis Branch
NOAA / NWS / NCEP / EMC
NCEP.list.WAVEWATCH@NOAA.gov
NCEP.list.waves@NOAA.gov

## Slide 2: Outline
Covered in this lecture:
  Compiling the code.
  Running the code.
  Optimizing parallel model implementations.
    Parallel implementation of individual grids (ww3_shel).
    Additional options in ww3_multi.
      Hybrid parallelization.
      Profiling.
      Memory use (+IO).
    Considerations and pitfalls.
    Future ….

## Slide 3: compiling
Parallel implementation of WAVEWATCH III
  Using MPI only, but code (switches) allow for other type of parallel architecture.
    MPI was the standard before, now is even more so.
    Thinking about shmem (Cray) style parallel implementation but never had the need to act on this.
  Not all codes use / can benefit from parallel implementation:
    Actual wave model codes ww3_shel, ww3_multi, …. will run much more efficient.
    Initialization code ww3_strt may need in some cases for memory use (rarely if ever used at NCEP).

## Slide 4: compiling
Make sure MPI is implemented correctly:
  Large majority of issues with MPI have been in MPI implementation:
    Even on our production IBM power series machines.
    Hope you have good IT support.

## Slide 5: compiling
Compile in several steps:
  Set switches for serial code (SHRD switch)
  Compile serial codes from scratch:
    Call w3_new to force complete compile of all routines (not strictly necessary).
    Call w3_make with or without program names to get base set of serial codes.
  Set switches for parallel code (DIST and MPI switch).
  Compile parallel codes:
    Compile selected codes only
      w3_make ww3_shel ww3_multi ….
    This will automatically recompile all used subroutines.
All this is done automatically in make_MPI.

## Slide 6: Running parallel
Running code in parallel depends largely on hardware and software on your computer.
  Generally there is a parallel operations environment:
    “poe” on IBM systems
    “mpirun” or other on Linux systems.
    Sometimes, environment needs to be started separately.
      mpdboot on UMD cluster.
    Check out with your system, IT support if you have it.
  There are some examples in the test scripts, particularly the ww3_multi and real-world test cases mww3_test_NN and mww3_case_NN.
  Pitfall: many duplicate output lines: you are running a serial code in a parallel environment …..

## Slide 7: Optimization
Three things to consider while
optimizing the implementation.
  General code optimization (no further discussion):
    Compiler options.
    Switches (2nd order versus 3rd order propagation, etc.)
    Spectral resolution.
    Time stepping.
  MPI optimization (no further discussion).
    Often overlooked, but can be very important on Linux systems.
  Application optimization (see below):
    Cannot do too much with ww3_shel, but will show techniques used here.
    Many additional options in ww3_multi.
Tolman, H. L., 2002: Parallel Computing, 28, 35-52.
Tolman, H. L., 2003: MMAB Tech. Note 228, 27 pp.

## Slide 8: ww3_shel
Physical space
Spectral space
directions
frequencies
The prognostic variable is the spectral wave energy density as a function of spatial and spectral coordinates and of time.

## Slide 9: ww3_shel
Propagation :
  By definition linear, nonlinear corrections possible.
  Covers all dimensions.
Physics :
  Wave growth and decay due to external factors :
    wind-wave interactions,
    wave-wave interactions,
    dissipation.
  Local in physical space.

## Slide 10: ww3_shel
Time splitting / Fractional steps.
Separate treatment of :
  physics (local),
  local propagation effects (change of direction or frequency),
  spatial propagation.
Each step consecutively operates on small subsets of data.
Entire model in core, memory requirements less than twice that of storing single state.

## Slide 11: ww3_shel
Physics involved suggest that grid points are distributed over processors rather than spectral components, particularly for the time splitting and source term integration techniques used in WAVEWATCH III.
"blocking"
"Scattering"

## Slide 12: ww3_shel
WAVEWATCH
Blocking :
  Only data at block bound. needed.
  Total amount of data comm. is a function of # of processes.
  Algorithm depends on actual prop. scheme.
Scattering :
  Full data transpose needed.
  Total amount of data comm. nearly constant.
  Algorithm inde- pendent of prop. scheme.
  Load balancing easier.

## Slide 13: ww3_shel
For WAVEWATCH III (ww3_shel)
the scattering method is used because :
  Compatibility with previous versions.
  Maximum flexibility and transparency of code (future physics and numerics developments).
  Feasibility based on estimates of amount of communication needed.
  MPI used for portability.

## Slide 14: ww3_shel
Standard optimization techniques :
  Non-blocking communication.
  Persistent communication, mainly for transparency of code.
Buffering of the data during transpose:
  Avoids idle CPU cycles during communication operations.
  Communication “hidden” behind calculations.
processors with native data
2
1
0
3
scatter
gather
buffer
buffer
buffer
active
at target processor
convert
convert
calculate propagation
1-D array with given spectral component for all sea points
Corresponding 2-D spatial wave field

## Slide 15: ww3_shel
Performance test case :
  Global model version with 288 x 157 spatial grid points (30,030 sea points) and 600 spectral components. 12 hour hindcast, 3 day forecast.
Resources :
  IBM RS6000 SP with Winterhawk nodes with 2 processors and 500 Mb memory and a NFS or GPFS file system.
  AIX version 4.3.
  xlf version 6.
Not always applicable to linux ….
MPI setup impact ….

## Slide 16
NFS
red : calculation only.
blue : model without output.
green : full model.
dashed and dotted lines :
efficiency required to match
Cray C90 with 1 or 12 CPUs

## Slide 17
GPFS
red : calculation only.
blue : model without output.
dashed and dotted lines :
efficiency required to match
Cray C90 with 1 or 12 CPUs

## Slide 18: ww3_multi
For mosaic approach, there are
other optimization options:
  Splitting grid in overlapping domains:
    Better local CFL time steps.
    Hybrid domain decomposition / data transpose.
      Presently being researched at NCEP.
  Running grids with same rank side-by-side on parts of communicator:
    Localizing communications.
    Amdahl's law generally favors running grids side-by-side on smaller number of processors over running in sequence over larger number of processors.

## Slide 19: ww3_multi
Splitting the communicator:
  Example from mww3_test_03, running three overlapping low resolution grids, with overlay of three overlapping high resolution grids.
    Example runs low1-3 serially on entire communicator.
    Example runs hgh1-3 side-by-side on fractions of communicator.
    Output can also go to dedicated processors.
from mww3_test_03 ww3_multi input file .....
$
’low1' 'no' 'no' ’no' 'no' 'no' 'no' 'no' 1 1 0.00 1.00 F
’low2' 'no' 'no' ’no' 'no' 'no' 'no' 'no' 1 1 0.00 1.00 F
’low3' 'no' 'no' ’no' 'no' 'no' 'no' 'no' 1 1 0.00 1.00 F
$
’hgh1' 'no' 'no' ’no' 'no' 'no' 'no' 'no' 2 1 0.00 0.33 F
’hgh2' 'no' 'no' ’no' 'no' 'no' 'no' 'no' 2 1 0.33 0.67 F
’hgh3' 'no' 'no' ’no' 'no' 'no' 'no' 'no' 2 1 0.67 1.00 F
$
Note: identical fractions = non-overlapping communicators

## Slide 20: ww3_multi
WAVEWATCH III log file version 4.08
=====================================================================
multi-grid model driver date : 2013/01/04
time : 11:01:35
. . . . .
Group information :
nr grids (part of comm.)
--------------------------------------------------------------------
1 1 (0.00-1.00)
2 2 (0.00-0.33) 3 (0.33-0.66) 4 (0.66-1.00)
--------------------------------------------------------------------
Resource assignement (processes) :
grid comp. grd pnt trk rst bpt prt
---------------------------------------------------
low0 001-012 011 --- --- --- --- ---
hgh1 001-004 003 --- --- --- --- ---
hgh2 005-008 007 --- --- --- --- ---
hgh3 009-012 011 --- --- --- --- ---
---------------------------------------------------
Running with or without output processor
WAVEWATCH III log file version 4.08
=====================================================================
multi-grid model driver date : 2013/01/04
time : 11:05:27
. . . . .
Group information :
nr grids (part of comm.)
--------------------------------------------------------------------
1 1 (0.00-1.00)
2 2 (0.00-0.33) 3 (0.33-0.66) 4 (0.66-1.00)
--------------------------------------------------------------------
Resource assignement (processes) :
grid comp. grd pnt trk rst bpt prt
---------------------------------------------------
low0 001-011 012 --- --- --- --- ---
hgh1 001-004 012 --- --- --- --- ---
hgh2 005-007 012 --- --- --- --- ---
hgh3 008-011 012 --- --- --- --- ---
---------------------------------------------------

## Slide 21: ww3_multi
Grid-level profiling:
  Compile under MPI with MPRF switch on.
  Run short piece of model, generating profiling data sets.
  Run GrADS script profile.gs to visualize:
  Example of NCEP’s original multi-grid wave model on next slide.
    8 grids.
    360 processors.
    Dedicated I/O processors.

## Slide 22: ww3_multi
regional
coastal
coupling
output
global
NCEP “multi_1” global model on IBM ca. 2008

## Slide 23: Memory use + IO
When running a grid on NAPROC processors,
each processor stores:
  NSEA/NAPROC spectra. (scaling)
  Output fields:
    Version 4.08 and earlier full fields. (not sc.)
    Version 4.09 and later:
      Sparse output fields (NSEA/NAPROC). (scaling)
      Full output fields (NSEA) in 1 processor only, only fields for selected output. (not sc.)
  Other outputs:
    Gathered in one processor, with some buffering to limit local memory use. (“scaling”)
  Work arrays, interpolation tables, … (not sc.)

## Slide 24: Memory use + IO
IO considerations: IO server type IOSTYP in ww3_shel and ww3_multi.
  0: No IO server process, use direct access write in restart file. Requires full parallel file system
  1: No IO server process, each output in single process.
  2: Single dedicated IO process for all output.
  3:Dedicated IO process for each separate IO type.
  In ww3_multi, all point output can go to dedicated processor
IO proc
full fields
1
sparse spectra
sparse fields
……
sparse spectra
sparse fields
naproc
sparse spectra
sparse fields
1
sparse spectra
sparse fields
2
sparse spectra
sparse fields
naproc
sparse spectra
sparse fields
……
sparse spectra
sparse fields
full fields
4.09 +
4.09 +

## Slide 25: Memory use + IO
IO considerations:
  Use IO server to manage memory use as well as faster IO.
    Combine with smart placement on nodes (e.g., less processes on node that does IO) leaves much flexibility for efficient loading of large grids.
  Use overlapping grids:
    Each grid has much smaller full field arrays.
    Stitch together later with ww3_gint.

## Slide 26: ww3_multi
Considerations and pitfalls:
  Intra-node and across-node communications are very different.
    Keeping grid on node may be important.
  Scaling on different systems is very different:
    IBM-SP versus Linux.
    Impact of file system.
    Optimization of MPI.
      Data transpose is many small messages, MPI needs to be tuned for this …
  For operational models, dimension for worst case:
    Profile without ice.
    Consider smallest grids with largest storms in consideration of load balancing.

## Slide 27: Optimization future
Working on the following:
  Hybrid domain decomposition / data transpose parallel using ww3_multi and automatic grid spitting code (under development).
  Provide some assessment of optimization for both climate (low-res, high-speed), and deterministic (high-res, high-speed) implementations.
Stay tuned !

## Slide 28: The end
End of lecture